## Slide 1: Introduction to Operating Systems CS/COE 1550
Fall 2021
Sherif Khattab
ksm73@pitt.edu
(Some slides are from Silberschatz, Galvin and Gagne ©2013)

## Slide 2: Announcements
Upcoming deadlines:
  4/22: Homework 12
  4/23: Lab 5
  4/26: Project 4 (File System)
  5/2: Quiz 4
  Tophat questions due one week after each lecture
OMETs
  1 bonus point when response rate >= 80%
  currently 26-27%

## Slide 3: Last Lecture …
File System Implementation
  Optimizing performance
    sector interleaving
    i-node grouping
    log-structured file system
  CD-ROM and SSD issues

## Slide 4: Muddiest Points
For the final, will it be the same as the midterm and only cover the material after the midterm?
Is there a scenario to use sector interleaving now ?
  how does sector interleaving increase performance?
grouping data on disk slide
  What is a cylinder group?
Flash Disks
  wear leveling
  Why does preventing writing 0s to 1s give better performance
  Why does flash file system work?
  A visual of wear leveling
sector implementation: what kinds of structures/logic would this involve?
Log-Structured File Systems
  What is the advantage of log structured file systems besides keeping old versions of files?
  does using the log structured file system lower disk utilization?

## Slide 5: Disks, cylinders, cylinder groups

## Slide 6: Wear leveling for SSDs

## Slide 7: Log Structured File System

## Slide 8: Today’s Agenda …
Low-level device driver issues
  memory-mapped vs port-mapped I/O
  3 Ways to read/write from an I/O Device
  Disk structure and scheduling

## Slide 9: Grouping data on disk

## Slide 10: Log-structured file systems
Trends in disk & memory
  Faster CPUs
  Larger memories
Result
  More memory -> disk caches can also be larger
  Increasing number of read requests can come from cache
  Thus, most disk accesses will be writes
LFS structures entire disk as a log
  All writes initially buffered in memory
  Periodically write these to the end of the disk log
  When file opened, locate i-node, then find blocks
Issue: what happens when blocks are deleted?

## Slide 11: CD-ROM recording
CD-ROM has data in a spiral
  Hard drives have concentric circles of data
One continuous track: just like vinyl records!
Pits & lands “simulated” with heat-sensitive material on CD-Rs and CD-RWs

## Slide 12: Flash File System
Wear Leveling
Count total writes per flash sector and attempt to balance across the whole disk

## Slide 13: Software Stack

## Slide 14: Device drivers
Device drivers go between device controllers and rest of OS
  Drivers standardize interface to widely varied devices
Device drivers communicate with controllers over bus
  Controllers communicate with devices themselves
User space
Kernel space
User program
Keyboard driver
Disk driver
Rest of the OS
Keyboard controller
Disk controller

## Slide 15: How are I/O devices connected?
Single-bus
  All memory accesses go over a shared bus
  I/O and RAM accesses compete for bandwidth
Dual-bus
  RAM access over high-speed bus
  I/O access over lower-speed bus
  Less competition
  More hardware (more expensive…)
CPU
Memory
I/O
CPU
Memory
I/O
This port allows I/O devices access into memory

## Slide 16: Device controllers
Electronic component controls the device
  May be able to handle multiple devices
  May be more than one controller per mechanical component (example: hard drive)
Controller's tasks
  Convert serial bit stream to block of bytes
  Perform error correction as necessary
  Make available to main memory
Block Devices
  A device that stores data in fixed‐sized blocks, each uniquely addressed, and can be randomly accessed
Character Devices
  Device that delivers or accepts a stream of characters

## Slide 17: Layers of I/O software
User-level I/O software & libraries
Device-independent OS software
Device drivers
Interrupt handlers
Hardware
Operating system (kernel)
User

## Slide 18: Anatomy of an I/O request

## Slide 19: Device Driver goals
Device independence
  Programs can access any I/O device
  No need to specify device in advance
Uniform naming
  Name of a file or device is a string or an integer
  Doesn’t depend on the machine (underlying hardware)
Error handling
  Done as close to the hardware as possible
  Isolate from higher-level software
Synchronous vs. asynchronous transfers
  Blocked transfers vs. interrupt-driven
Buffering
  Data coming off a device cannot be stored in final destination
Sharable vs. dedicated devices

## Slide 20: Memory-Mapped vs. separate I/O Space
Separate I/O & memory space
0xFFF…
0
Memory
I/O ports
Memory-mapped I/O
Hybrid: both memory-mapped & separate spaces

## Slide 21: Example: Dynamic Frequency on XScale

## Slide 22: Programmed I/O example: printing a page
Printed page
ABCD EFGH
Kernel
User
A
Printed page
ABCD EFGH
ABCD EFGH
AB
Printed page
ABCD EFGH
ABCD EFGH

## Slide 23: Polling
copy_from_user (buffer, p, count); // copy into kernel buffer
for (j = 0; j < count; j++) { // loop for each char
while (*printer_status_reg != READY)
; // wait for printer to be ready
*printer_data_reg = p[j]; // output a single character
}
return_to_user();

## Slide 24: Hardware’s view of interrupts
Bus

## Slide 25: Interrupt-driven I/O
copy_from_user (buffer, p, count);
j = 0;
enable_interrupts();
while (*printer_status_reg != READY)
;
*printer_data_reg = p[0];
scheduler(); // and block user
if (count == 0) {
unblock_user();
} else {
j++;
*printer_data_reg = p[j];
count--;
}
acknowledge_interrupt();
return_from_interrupt();
Code run by system call
Code run at interrupt time
(Interrupt handler)

## Slide 26: What happens on an interrupt
Set up stack for interrupt service procedure
Ack interrupt controller, reenable interrupts
Copy registers from where saved
Run service procedure
(optional) Pick a new process to run next
Set up MMU context for process to run next
Load new process' registers
Start running the new process

## Slide 27: Direct Memory Access (DMA) operation

## Slide 28: I/O using DMA
copy_from_user (buffer, p, count);
set_up_DMA_controller();
scheduler(); // and block user
acknowledge_interrupt();
unblock_user();
return_from_interrupt();
Code run by system call
Code run at interrupt time

## Slide 29: Why a standard driver interface?
Non-standard driver interfaces
Standard driver interfaces

## Slide 30: Buffering device input
User space
Kernel space
User space
Kernel space
User space
Kernel space
User space
Kernel space
Unbuffered input
Buffering in user space
Buffer in kernel Copy to user space
Double buffer in kernel
1
2
1
3
2

## Slide 31: Disk drive structure
Data stored on surfaces
  Up to two surfaces per platter
  One or more platters per disk
Data in concentric tracks
  Tracks broken into sectors
    256B-1KB per sector
  Cylinder: corresponding tracks on all surfaces
Data read and written by heads
  Actuator moves heads
  Heads move in unison
sector
cylinder
platter
spindle
track
head
actuator
surfaces

## Slide 32: Disk scheduling algorithms
Schedule disk requests to minimize disk seek time
  Seek time increases as distance increases (though not linearly)
  Minimize seek distance -> minimize seek time
Disk seek algorithm examples assume a request queue & head position (disk has 200 cylinders)
  Queue = 100, 175, 51, 133, 8, 140, 73, 77
  Head position = 63
100
175
51
133
8
140
73
77
read/write head position
disk requests
(cylinder in which block resides)
Outside edge
Inside edge

## Slide 33: First-Come-First Served (FCFS)
Requests serviced in the order in which they arrived
  Easy to implement!
  May involve lots of unnecessary seek distance
Seek order = 100, 175, 51, 133, 8, 140, 73, 77
Seek distance = (100-63) + (175-100) + (175-51) + (133-51) + (133-8) + (140-8) + (140-73) + (77-73) = 646 cylinders
100
175
51
133
8
140
73
77
read/write head start

## Slide 34: Shortest Seek Time First (SSTF)
Service the request with the shortest seek time from the current head position
  Form of SJF scheduling
  May starve some requests
Seek order = 73, 77, 100, 133, 140, 175, 51, 8
Seek distance = 10 + 4 + 23 + 33 + 7 + 35 + 124 + 43 = 279 cylinders
100
175
51
133
8
140
73
77
read/write head start

## Slide 35: SCAN (elevator algorithm)
Disk arm starts at one end of the disk and moves towards the other end, servicing requests as it goes
  Reverses direction when it gets to end of the disk
  Also known as elevator algorithm
Seek order = 51, 8, 0 , 73, 77, 100, 133, 140, 175
Seek distance = 12 + 43 + 8 + 73 + 4 + 23 + 33 + 7 + 35 = 238 cyls
100
175
51
133
8
140
73
77
read/write head start

## Slide 36: C-SCAN
Identical to SCAN, except head returns to cylinder 0 when it reaches the end of the disk
  Treats cylinder list as a circular list that wraps around the disk
  Waiting time is more uniform for cylinders near the edge of the disk
Seek order = 73, 77, 100, 133, 140, 175, 199, 0, 8, 51
Distance = 10 + 4 + 23 + 33 + 7 + 35 + 24 + 199 + 8 + 43 = 386 cyls
100
175
51
133
8
140
73
77
read/write head start

## Slide 37: C-LOOK
Identical to C-SCAN, except head only travels as far as the last request in each direction
  Saves seek time from last sector to end of disk
Seek order = 73, 77, 100, 133, 140, 175, 8, 51
Distance = 10 + 4 + 23 + 33 + 7 + 35 + 167 + 43 = 322 cylinders
100
175
51
133
8
140
73
77
read/write head start