## Slide 1: Introduction to Operating Systems CS/COE 1550
Fall 2021
Sherif Khattab
ksm73@pitt.edu
(Some slides are from Silberschatz, Galvin and Gagne ©2013)

## Slide 2: Announcements
Homework 1 is due this Friday at 11:59 pm
  Special late deadline until Monday 2/8 at 11:59 pm
Tophat questions assigned as homework
Lab 1 is up (with autograder on Gradescope)
  Using GitHub Classroom
  Explained in this week’s recitation
Project 1 will be up this Friday

## Slide 3: Last Lecture …
Process scheduling
Process creation and termination

## Slide 4: Muddiest Points
Scheduling
  Queues
  How processes actually get scheduled by the scheduler
  How to invoke the schedulers
  What is the definition degree of multiprogramming?
  What is the difference between the short-term and medium-term schedulers. They seem to both do similar things
  How the CPU determines which processes can be safely swapped out without affecting performance.
  Moving of registers
fork()
  Tracing
  IDs of forked processes, and forks of forks
  zombie vs orphan
  How the parent knows how long to wait when using the wait() syscall
  pid for children
exec()
  how it works
  difference between fork() and exec()
understand the whole process with CODE

## Slide 5: Muddiest points
Xv6 code for context switching
Process lifecycle
CPU mode switching in context switching
What is inside PCB
Switching register sets in context switching
the code plus the diagram side by side
Determining when a context switch is actually required - if it's needed between each individual process regardless of user/kernel bit
monotlithic vs microkernel
  Pros and cons
  What a microkernel OS would look like in practice
the two tophat questions we all got wrong about immediately performing instructions in priviledged/non-priviledged mode
How long the context switching takes on average compared to the processes themselves.

## Slide 6: fork() tracing

## Slide 7: fork()’s of fork()’s

## Slide 8: Orphan vs. Zombie Processes

## Slide 9: Xv6 Code Walkthrough
Context switching
  Calling of the swtch routine
fork()
exit()
wait()

## Slide 10: Today ….
Spinlocks
  How to use
  How to implement
Semaphores
  How to use
  How to implement

## Slide 11: Why do we need Synchronization?
Each process operates sequentially
All is fine until processes want to share data
  Exchange data between multiple processes
  Allow processes to navigate critical regions
  Maintain proper sequencing of actions in multiple processes
These issues apply to threads as well
  Threads can share data easily (same address space)
  Other two issues apply to threads

## Slide 12: Example: bounded buffer problem
Shared variables const int n; typedef … Item; Item buffer[n]; int in = 0, out = 0, counter = 0;
Atomic statements:
Counter += 1;
Counter -= 1;
Consumer
Item citm; while (1) { while (counter == 0) ; citm = buffer[out]; out = (out+1) % n;
counter -= 1;
… consume the item in citm … }
Producer
Item pitm; while (1) { … produce an item into pitm … while (counter == n) ; buffer[in] = pitm; in = (in+1) % n;
counter += 1; }

## Slide 13: Problem: race conditions
Cooperating processes share storage (memory)
Both may read and write the shared memory
Problem: can’t guarantee that read followed by write is atomic
  Ordering matters!
This can result in erroneous results!
We need to eliminate race conditions…
R1 <= x
R1 = R1+1
R1 => x
R3 <= x
R3 = R3+1
R3 => x
P1
P2
x=3
x=5
R1 <= x
R1 = R1+1
R1 => x
R3 <= x
R3 = R3+1
R3 => x
x=6!

## Slide 14: Critical regions
Use critical regions to provide mutual exclusion and help fix race conditions
Four conditions to provide mutual exclusion
  No two processes simultaneously in critical region
  No assumptions made about speeds or numbers of CPUs
  No process running outside its critical region may block another process
  No process must wait forever to enter its critical region
Process A
Process B
B blocked
A enters critical region
B tries to enter critical region
B enters critical region
A leaves critical region
B leaves critical region
Time

## Slide 15: Using Spinlocks
Code for process Pi
While(1){
  Lock(lock)
  // critical section
  Unlock(lock);
  // remainder of code
  }
}
Spinlock lock;

## Slide 16: Spinlock implementation (1/2)
Solution: use hardware
Several hardware methods
  Test & set: test a variable and set it in one instruction
  Atomic swap: switch register & memory in one instruction
  Turn off interrupts: process won’t be switched out unless it asks to be suspended
Can be in user land

## Slide 17: Atomic operations
If done in one instruction, then not interruptible

## Slide 18: Spinlock implementation (2/2)
Single shared variable: lock
requires busy waiting, but code is much simple
Two versions
  Test and set
  Swap
Works for any number of processes
Possible problem with requirements
  can lead to unbounded waiting
Lock(){
while (TestAndSet(lock))
;
}
Unlock(){
lock = 0;
}
Lock(){
while (Swap(lock,1) == 1)
;
}
Unlock(){
lock = 0;
}
int lock = 0;

## Slide 19: Semaphores
Solution: use semaphores
  Synchronization mechanism that doesn’t require busy waiting
Implementation
  Semaphore S accessed by two atomic operations
    Down(S): while (S<=0) {}; S-= 1;
    Up(S): S+=1;
  Down() is another name for P()
  Up() is another name for V()
  Modify implementation to eliminate busy wait from Down()